## Slide 1: Module 5: Network Security Infrastructure

## Slide 2: Objectives
Module Objective: Explain how devices and services are used to enhance network security.
Topic Title | Topic Objective
Network Topologies | Explain how network designs influence the flow of traffic through the network.
Security Devices | Explain how specialized devices are used to enhance network security.
Security Services | Explain how network services enhance network security.
Notes: 2
CyberOps Associate v1.0
12 – Network Security Infrastructure
12.0 – Introduction
12.0.2 – What Will I Learn in this Module?

## Slide 3
Network Security Infrastructure Network Representations
Network diagrams, often called topology diagrams, use symbols to represent different devices and connections within the network.
The important terminologies to be known include:
  Network Interface Card (NIC)
  Physical Port
  Interface
Note: The terms port and interface are often used interchangeably.
Notes: 12 – Network Security Infrastructure
12.1– Network Topologies
12.1.1– Network Representations

## Slide 4
Network Security Infrastructure Topology Diagrams
Physical topology diagrams illustrate the physical location of intermediary devices and cable installation.
Logical topology diagrams illustrate devices, ports, and the addressing scheme of the network.
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.2 – Topology Diagrams

## Slide 5
Network Security Infrastructure Networks of Many Sizes
Small Home Networks – connect a few computers to each other and the Internet.
Small Office and Home Office (SOHO) – enables computer within a home, office or remote office to connect to a corporate network, or access centralized, shared resources.
Medium to Large Networks – can have many locations with hundreds or thousands of interconnected computers.
World Wide Networks – connects hundreds of millions of computers world-wide – such as the internet.
Small Home SOHO
Medium/Large World Wide
Notes: 12 – Network Security Infrastructure
12.1– Network Topologies
12.1.3 – Networks of Many Sizes

## Slide 6
Network Topologies LANs and WANs
Network infrastructures vary greatly in terms of:
  Size of the area covered
  Number of users connected
  Number and types of services available
  Area of responsibility
The two most common types of network infrastructures are
  Local Area Networks (LANs)
  Wide Area Networks (WANs)
LANs connected to a WAN
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.4 – LANs and WANs

## Slide 7
Network Topologies LANs and WANs (Contd.)
A LAN is a network infrastructure that spans a small geographical area.
A WAN is a network infrastructure that spans a wide geographical area.
LAN | WAN
Interconnect end devices in a limited area. | Interconnect LANs over wide geographical areas.
Administered by a single organization or individual. | Typically administered by multiple service providers.
Provide high-speed bandwidth to internal end devices and intermediary devices. | Typically provide slower speed links between LANs.
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.4 – LANs and WANs

## Slide 8
Network Security Infrastructure The Three-Layer Network Design Model
The campus wired LAN uses a hierarchical design model to separate the network topology into modular groups or layers.
The hierarchical LAN design includes three layers:
Access - Provides endpoints and users direct access to the network.
Distribution - Aggregates access layers and provides connectivity to services.
Core - Provides connectivity between distribution layers for large LAN environments.
Hierarchical Design Model
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.5 – The Three-Layer Network Design Model

## Slide 9
Network Security Infrastructure The Three-Layer Network Design Model (Contd.)
Although the hierarchical model has three layers, some smaller enterprise networks may implement a two-tier hierarchical design.
In this two-tier hierarchical design, the core and distribution layers are collapsed into one layer, thus reducing cost and complexity.
Collapsed Core
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.5 – The Three-Layer Network Design Model

## Slide 10
Network Security Infrastructure Common Security Architectures
Firewall design is primarily about device interfaces permitting or denying traffic based on the source, the destination, and the type of traffic.
The three firewall designs are:
Public and Private
The public network (or outside network) is untrusted, and the private network (or inside network) is trusted.
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.7 – Common Security Architectures

## Slide 11
Network Security Infrastructure Common Security Architectures (Contd.)
Demilitarized Zone (DMZ)
A firewall design where there is typically one:
Inside interface connected to the private network
Outside interface connected to the public network
DMZ interface
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.7 – Common Security Architectures

## Slide 12
Network Security Infrastructure Common Security Architectures (Contd.)
Zone-based Policy Firewalls (ZPFs)
ZPFs use the concept of zones to provide additional flexibility.
A zone is a group of one or more interfaces that have similar functions or features.
Zones help to specify where a Cisco IOS firewall rule or policy should be applied.
Notes: 12 – Network Security Infrastructure
12.1 – Network Topologies
12.1.7 – Common Security Architectures
12.1.8 – Check your Understanding - Identify the Network Topology

## Slide 13
Security Devices Firewalls
A firewall is a system, or group of systems, that enforces an access control policy between networks.
Common Firewall Properties:
Resistant to network attacks
The only transit point between internal corporate networks and external networks because all traffic flows through the firewall
Enforce the access control policy
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.2 – Firewalls

## Slide 14
Security Devices Firewalls (Contd.)
Following are the benefits and limitations of firewalls:
Firewall Benefits | Firewall Limitations
Prevent the exposure of sensitive hosts, resources, and applications to untrusted users. | A misconfigured firewall can have serious consequences for the network, such as becoming a single point of failure.
Sanitize protocol flow, which prevents the exploitation of protocol flaws. | The data from many applications cannot be passed over firewalls securely.
Block malicious data from servers and clients. | Users might proactively search for ways around the firewall to receive blocked material, which exposes the network to potential attack.
Reduce security management complexity. | Network performance can slow down.
 | Unauthorized traffic can be tunnelled or hidden as legitimate traffic through the firewall.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.2 – Firewalls

## Slide 15
Security Devices Firewall Type Descriptions
The different types of firewalls are:
Packet Filtering (Stateless) Firewall
Packet Filtering firewalls are part of a router firewall, which permits or denies traffic based on Layer 3 and Layer 4 information.
They are stateless firewalls that use a simple policy table look-up that filters traffic based on specific criteria.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.3 – Firewall Type Descriptions

## Slide 16
Security Devices Firewall Type Descriptions (Contd.)
Stateful Firewalls
Stateful firewalls are the most versatile and the most common firewall technologies in use.
These firewalls provide stateful packet filtering by using connection information maintained in a state table.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.3 – Firewall Type Descriptions

## Slide 17
Security Devices Firewall Type Descriptions (Contd.)
Application gateway firewall (proxy firewall)
Application gateway firewall filters information at Layers 3, 4, 5, and 7 of the OSI reference model.
Most of the firewall control and filtering is done in the software.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.3 – Firewall Type Descriptions

## Slide 18
Security Devices Firewall Type Descriptions (Contd.)
Next-generation firewalls (NGFW)
NGFW go beyond stateful firewalls by providing:
Integrated intrusion prevention
Application awareness and control to see and block risky apps
Upgrade paths to include future information feeds
Techniques to address evolving security threats
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.3 – Firewall Type Descriptions

## Slide 19
Security Devices Firewall Type Descriptions (Contd.)
Other methods of implementing firewalls include:
  Host-based (server and personal) firewall - A PC or server with firewall software running on it.
  Transparent firewall - Filters IP traffic between a pair of bridged interfaces.
  Hybrid firewall - A combination of various firewall types.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.3 – Firewall Type Descriptions
12.2.4 – Check Your Understanding - Identify the Type of Firewall

## Slide 20: Firewalls in Network Design Layered Defense
A layered defense uses different types of firewalls that are combined in layers to add depth to the security of an organization. Policies can be enforced between the layers and inside the layers. The following example shows four layers of security.
Network Core security - Protects against malicious software and traffic anomalies, enforces network policies, and ensures survivability
Perimeter security - Secures boundaries between zones
Communications security - Provides information assurance
Endpoint security - Provides identity and device security policy compliance

## Slide 21: Firewalls in Network Design Layered Defense(Cont.)
This partial list of best practices can serve as a starting point for a firewall security policy.
  Position firewalls at security boundaries. Firewalls are a critical part of network security, but it is unwise to rely exclusively on a firewall for security.
  Deny all traffic by default.
  Permit only services that are needed.
  Ensure that physical access to the firewall is controlled.
  Regularly monitor firewall logs.
  Practice change management for firewall configuration changes.
  Remember that firewalls primarily protect from technical attacks originating from the outside.

## Slide 22: IDS and IPS Characteristics Zero-Day Attacks
A zero-day attack is a cyberattack that tries to exploit software vulnerabilities that are unknown or undisclosed by the software vendor. The term zero-day describes the moment when a previously unknown threat is identified.
Notes: One approach to prevent malware exploits is for an administrator to continuously monitor the network and analyze the log files generated by network devices. Security operations center (SOC) tools, such as security information and event management (SIEM) and security orchestration, automation, and response (SOAR) systems automate the log file gathering and analysis process. It has become an accepted fact that malware will enter the network despite the best defenses. For this reason, a multilayered approach to malware protection must be employed. Logfiles generated by devices at each layer will help to identify whether an exploit has occurred, the diagnostic features of the exploit, and the extent of the damage within the enterprise. The information gathered in logfiles will also help to inform measures taken in response to the exploit, such as containment and mitigation.
Intrusion Detection Systems (IDS) were implemented to passively monitor the traffic on a network. The figure shows that an IDS-enabled device copies the traffic stream and analyzes the copied traffic rather than the actual forwarded packets.

## Slide 23
Security Devices Intrusion Prevention and Detection Devices
A networking architecture paradigm shift is required to defend against fast-moving and evolving attacks. This must include cost effective and prevention systems such as:
Intrusion Detection Systems (IDS)
Intrusion Prevention Systems (IPS)
The network architecture integrates these solutions into the entry and exit points of the network.
The figure shows how an IPS device handles malicious traffic.
Notes: IDS and IPS technologies are both deployed as sensors. An IDS or IPS sensor can be in the form of several different devices:
A router configured with IPS software
A device specifically designed to provide dedicated IDS or IPS services
A hardware module installed in an adaptive security appliance (ASA), switch, or router
IDS and IPS technologies use signatures to detect patterns in network traffic. A signature is a set of rules that an IDS or IPS uses to detect malicious activity. Signatures can be used to detect severe breaches of security, to detect common network attacks, and to gather information. IDS and IPS technologies can detect atomic signature patterns (single-packet) or composite signature patterns (multi-packet).

## Slide 24
Security Devices Advantages and Disadvantages of IDS and IPS
The table lists the advantages and disadvantages of IDS and IPS:
Solution | Advantages | Disadvantages
IDS | No Impact on network (latency, jitter) No Network impact if there is a sensor failure No network impact if there is sensor overload | Response action cannot stop trigger packets Correct tuning required for response actions More vulnerable to network security evasion techniques
IPS | Stops trigger packets Can use stream normalization techniques | Sensor issues might affect network traffic Sensor overloading impacts the network Some impact on network (latency, jitter)
Deployment Consideration:
IPS and IDS technologies can complement each other.
Deciding which implementation to use is based on the security goals of the organization as stated in their network security policy.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.6 – Advantages and Disadvantages of IDS and IPS

## Slide 25
Security Devices Types of IPS
There are two primary kinds of IPS :
  Host-based IPS
  Network-based IPS
Host-based IPS (HIPS)
HIPS is a software installed on a host to monitor and analyze suspicious activity.
Advantages | Disadvantages
Provides protection specific to a host operating system Provides operating system and application level protection Protects the host after the message is decrypted | Operating system dependent Must be installed on all hosts
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.7 – Types of IPS

## Slide 26
Security Devices Types of IPS (Contd.)
Network-based IPS
Network-based IPS are Implemented using a dedicated or non-dedicated IPS device.
Host-based IDS/IPS solutions are integrated with a network-based IPS implementation to ensure a robust security architecture.
Sensors detect malicious and unauthorized activity in real time and can take action when required.
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.7 – Types of IPS

## Slide 27: Snort IPS
Snort is the most widely deployed IPS solution in the world. It is an open source network IPS that performs real-time traffic analysis and generates alerts when threats are detected on IP networks. It can also perform protocol analysis, content searching or matching, and detect a variety of attacks and probes, such as buffer overflows, stealth port scans, and so on.
There are currently more than 30,000 signatures in the Snort rule set. It also supports the ability to customize rule sets and provides centralized deployment and management capabilities.
Snort can be enabled in either of the following modes:
IDS mode - Snort inspects the traffic and reports alerts, but does not take any action to prevent attacks.
IPS mode - In addition to intrusion detection, actions are taken to prevent attacks.
In the network intrusion detection and prevention mode, Snort performs the following actions:
Monitors network traffic and analyzes against a defined rule set.
Performs attack classification.
Invokes actions against matched rules.
The Snort IPS monitors the traffic and reports events to an external log server or the IOS syslog. Enabling logging to the IOS syslog may impact performance due to the potential volume of log messages. External third-party monitoring tools that support Snort logs can be used for log collection and analysis.

## Slide 28
Security Devices Specialized Security Appliances
Few examples of specialized security appliances.
Cisco Advanced Malware Protection (AMP) | Cisco Web Security Appliance (WSA) | Cisco Email Security Appliance (ESA)
An enterprise-class advanced malware analysis and protection solution | A secure web gateway that combines leading protections to help organizations address the growing challenges of securing and controlling web traffic | ESA/Cisco Cloud Email Security helps to mitigate email-based threats and the ESA defends mission-critical email systems
It provides comprehensive malware protection for organizations before, during, and after an attack | Protects the network by automatically blocking risky sites and testing unknown sites before allowing users to access them | Constantly updated by real-time feeds from Cisco Talos, which detects and correlates threats using a worldwide database monitoring system
 |  | Features: Global threat intelligence, Spam blocking, Advanced Malware Protection, Outbound Message Control
Notes: 12 – Network Security Infrastructure
12.2 – Security Devices
12.2.8 – Specialized Security Appliances
12.2.9 – Check Your Understanding - Compare IDS and IPS Characteristics

## Slide 29
Security Services Traffic Control with ACLs
An Access Control List (ACL) is a series of commands that control whether a device forwards or drops packets based on information found in the packet header.
When configured, ACLs perform the following tasks:
Limit network traffic to increase network performance.
Provide traffic flow control.
Provide basic level of security for network access.
Filter traffic based on traffic type.
Screen hosts to permit or deny access to network services.
Sample Topology with ACLs applied to routers R1, R2, and R3.
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.2 – Traffic Control with ACLs

## Slide 30
Security Services ACLs: Important Features
The two types of Cisco IPv4 ACLs are:
Standard ACL - Used to permit or deny traffic only from source IPv4 addresses.
Extended ACL - Filters IPv4 packets based on several attributes that include:
Protocol type
Source IPv4 address
Destination IPv4 address
Source TCP or UDP ports
Destination TCP or UDP ports
Optional protocol type information for finer control
Standard and extended ACLs can be created using either a number or a name to identify the ACL and its list of statements.
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.3 – ACLs: Important Features

## Slide 31
Security Services SNMP
Simple Network Management Protocol (SNMP) is an application layer protocol that provides a message format for communication between managers and agents.
It allows network administrators to perform the following:
Manage end devices such as servers, workstations, routers, switches, and security appliances, on an IP network.
Monitor and manage network performance.
Find and solve network problems.
Plan for network growth.
The SNMP system consists of two elements:
SNMP manager: Runs SNMP management software.
SNMP agents: Nodes being monitored and managed.
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.5 – SNMP

## Slide 32
Security Services Port Mirroring
Port mirroring is a feature that allows a switch to make duplicate copies of traffic passing through a switch, and then sending it out a port with a network monitor attached.
Traffic Sniffing Using a Switch
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.7 – Port Mirroring

## Slide 33
Security Services Syslog Servers
The most common method of accessing system messages is to use a protocol called syslog.
The Syslog protocol allows networking devices to send their system messages across the network to syslog servers.
It provides three primary functions:
The ability to gather logging information for monitoring and troubleshooting
The ability to select the type of logging information that is captured
The ability to specify the destination of captured syslog messages
Syslog
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.8 – Syslog Servers

## Slide 34
Security Services NTP
It is important to synchronize the time across all devices on the network. The date and time settings on a network device can be set using one of two methods:
  Manual configuration of the date and time
  Configuring the Network Time Protocol (NTP)
NTP networks use a hierarchical system of time sources, where each level in this system is called a stratum. NTP servers are arranged in three levels known as strata:
  Stratum 0: An NTP network gets the time from authoritative time sources.
  Stratum 1: Devices are directly connected to the authoritative time sources.
  Stratum 2 and lower strata: Stratum 2 devices, such as NTP clients, synchronize their time using the NTP packets from stratum 1 servers.
NTP Stratum Levels
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.9 – NTP

## Slide 35
Security Services AAA Servers
The below table lists the three independent security functions provided by the AAA architectural framework.
Functions | Description
Authentication | Users and administrators must prove that they are who they say they are. Authentication can be established using username and password combinations, challenge and response questions, token cards, and other methods. AAA authentication provides a centralized way to control access to the network.
Authorization | After the user is authenticated, authorization services determine which resources the user can access and which operations the user is allowed to perform. An example is “User ‘student’ can access host serverXYZ using SSH only.”
Accounting | Accounting records what the user does, including what is accessed, the amount of time the resource is accessed, and any changes that were made. Accounting keeps track of how network resources are used. An example is "User ‘student’ accessed host serverXYZ using SSH for 15 minutes."
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.10 – AAA Servers

## Slide 36
Security Services AAA Servers (Contd.)
The below table lists the difference between Terminal Access Controller Access-Control System Plus (TACACS+) and Remote Authentication Dial-In User Service (RADIUS) protocols.
 | TACACS+ | RADIUS
Functionality | Separates AAA according to the AAA architecture, | Combines authentication and authorization but separates accounting,
Standard | Mostly Cisco supported | Open/RFC standard
Transport | TCP | UDP
Protocol CHAP | Bidirectional challenge and response as used in Challenge Handshake Authentication Protocol (CHAP) | Unidirectional challenge and response from the RADIUS security server to the RADIUS client
Confidentiality | Entire packet encrypted | Password encrypted
Customization | Provides authorization of router commands on per-user or per-group basis | No option to authorize router commands on a per-user or per-group basis
Accounting | Limited | Extensive
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.10 – AAA Servers

## Slide 37
Security Services VPN
A VPN is a private network that is created over a public network (usually the internet).
A VPN uses virtual connections routed through the Internet from the organization to the remote site.
A VPN is a communications environment in which access is strictly controlled to permit peer connections within a defined community of interest.
Confidentiality is achieved by encrypting the traffic within the VPN.
In short, VPN connects two endpoints over a public network, to form a logical connection which can be made at Layer 2 or Layer 3.
Virtual Private Network
Notes: 12 – Network Security Infrastructure
12.3 – Security Services
12.3.11 – VPN
12.3.12 – Check Your Understanding - Identify the Network Security Device or Service

## Slide 38
Network Security Infrastructure Summary What Did I Learn in this Module?
    Networks are typically represented as physical and logical topologies.
    A physical topology represents physical connections and how end devices are connected whereas a logical topology refers to the standards and protocols that devices use to communicate.
    The two most common types of network infrastructures are LANs and WANs.
    The campus wired LAN design consists of hierarchical layers (access, distribution, core) with each layer assigned specific functions.
    Common security architectures define the boundaries of traffic entering and leaving the network.
    The different types of firewalls are Packet filtering firewalls, stateful inspection firewall, Application gateway firewalls, Next-generation firewalls.
Notes: 12 – Network Security Infrastructure
12.4 – Network Security Infrastructure Summary
12.4.1– What Did I Learn in this Module?

## Slide 39
Network Security Infrastructure Summary What Did I Learn in this Module? (Contd.)
    Intrusion prevention systems (IPS) and intrusion detection systems (IDS) are used to detect potential security risks and alert/stop unsafe traffic.
    Specialized security appliances are available including Cisco Advanced Malware Protection (AMP), Cisco Web Security Appliance (WSA), and Cisco Email Security Appliance (WSA).
    ACLs are a series of statements that control whether a device forwards or drops packets based on information found in the packet header.
    SNMP enables network administrators to monitor and manage network performance, find and solve network problems, and plan for network growth.
    NetFlow provides statistics on packets that are flowing through a Cisco router or multilayer switch.
    Port mirroring is a feature that allows a switch to make duplicate copies of traffic that is passing through the switch, and then send it out a port that has a network monitor attached.
Notes: 12 – Network Security Infrastructure
12.4 – Network Security Infrastructure Summary
12.4.1– What Did I Learn in this Module?

## Slide 40
Network Security Infrastructure Summary What Did I Learn in this Module? (Contd.)
    Syslog servers compile and provide access to the system messages generated by networking devices.
    NTP synchronizes the system time across all devices on the network to ensure accurate and consistent timestamping of system messages.
    AAA is a framework for configuring user authentication, authorization, and accounting services. It typically uses a TACACS+ or RADIUS server for this purpose.
    VPNs are private networks that are created between two endpoints across a public network.
Notes: 12 – Network Security Infrastructure
12.4 – Network Security Infrastructure Summary
12.4.1– What Did I Learn in this Module?
12.4.2 – Module 12: Network Security Infrastructure Quiz